## Slide 1: IIG Operational Activity hands On-1
Muntasir Khan
Sadia Safwat
Md. Shohel Rana

## Slide 2: Topic
BW: Internet,Youtube
Client Connectivity: Metro,Core(Single,Dual)
SFP 1Gbps: 1310nm,1550nm
SFP 10Gbps: 1270,1330nm

## Slide 3: Operational issues
Power (dB) check on Physical link
Prefix Permit (APNIC)
Interface Configuration & P2P check
BGP configuration
Client prefix recv. and global propagation
Route Advertisement
BW Policy
MRTG
Client add on Nagois server
VC/CC permit
High latency, browsing problem
Packet loss, download ,upload problem
Youtube BW problem
Destination/website unreachable
BTRC URL block
IP blacklisted
Interface shut/no shut
BW fall, link down, link flap

## Slide 4: Power Check
Cisco router: ISO,XR
show controllers Te0/0/0/0 phy
Cisco router: IOS XE
sh hw-module subslot 1/1 transceiver 0 status
Cisco SW : Cisco 4500,3800ME
sh interfaces Te1/18 transceiver
Cisco SW 9000 Nexus
show interface Eth1/36 transceiver details
BDCOM
Show interface tg1/1

## Slide 5: Prefix Permit
Check the client prefix for Origin As in Apnic website
Add client prefix list
Add AS in AS-SET in IIG & ITC Network
IIG: AS58717:AS-SUMMITCOMMUNICATIONS-BD
ITC: AS132884:AS-CUSTOMERS
Check route object for prefix
http://www.radb.net
https://www.apnic.net/
What is route object?
Each route on the internet originated by an AS is specified using a route object in the RIR database that the AS belongs to according to the region. The "route:" attribute is the address prefix of the route and the "origin:" attribute is the AS number of the AS that originates the route into the internet.
Mail to BSCCL,Singtel,BTTB to permit Prefix
Upstream confirmation
https://www.site24x7.com/tools/ipv4-subnetcalculator.html

## Slide 6: Interface Configuration
Port Configuration:
SCL#conf t
Enter configuration commands, one per line. End with CNTL/Z.
SCL(config)#interface Gi3/0/5
SCL(config-if)#description @@ TEST @@
SCL(config-if)#ip address 192.168.229.1 255.255.255.252
SCL(config-if)#service-policy input 10mb
SCL(config-if)#service-policy output 10mb
SCL(config-if)#no shutdown
SCL(config-if)#end
Sub-interface Configuration:
SCL#conf t
interface Bundle-Ether20.141
description @@ COL-CTG-SEC @@
encapsulation dot1Q 141
ipv4 address 103.26.246.109 255.255.255.252
commit

## Slide 7: E-BGP configuration IPv4 & IPv6
conf t
router bgp 58717
neighbor 103.26.246.110
remote-as 38592
description COL-CTG-SEC
address-family ipv4 unicast
route-policy CTG-COL-IN in
route-policy DEFAULT-ONLY out
soft-reconfiguration inbound always
commit
end
sh running-config router bgp 58717 neighbor 103.26.246.110
configure terminal
router bgp 58717
neighbor 2405:1500:30:1::46
remote-as 58889
description @@ ZX-IPV6-SEC @@
address-family ipv6 unicast
route-policy ZX-SEC-IPV6-PREFIX in
route-policy IPV6-DEFAULT-ONLY out
soft-reconfiguration inbound always
commit
end
sh bgp ipv6 unicast summary

## Slide 8: Prefix Permit
To create a new prefix set:
configure terminal
prefix-set COL-SEC-IN
103.76.240.0/22 le 24
end-set
commit
end
to add new prefix in the prefix set:
edit prefix-set COL-SEC-IN
show RPl prefix-set COL-SEC-IN
Fri Jun 3 12:10:55.609 UTC
prefix-set COL-SEC-IN
202.65.168.0/21 le 24,
101.2.160.0/21 le 24,
103.5.232.0/22 le 24,
203.82.200.0/21 le 24,
163.47.84.0/22 le 24,
119.10.172.0/22 le 24
end-set
configure Terminal
prefix-set ZX-SEC-IPV6-PREFIX
2401:1980::/32 le 48
exit
commit
end

## Slide 9: Route-Policy
how to create route policy:
configure t
route-policy CTG-COL-IN
if destination in COL-SEC-IN then
set local-preference 1000
set community TO-ALL
pass
else
drop
endif
end-policy
!
commit
end
configure terminal
route-policy ZX-SEC-IPV6-PREFIX
if destination in ZX-SEC-IPV6-PREFIX then
set local-preference 1000
set community TO-ALL
else
drop
endif
end-policy
!
commit
end

## Slide 10: Prefix recv
RP/0/RSP0/CPU0:PALTAN-IIG-AGG#show bgp ipv4 unicast neighbors 103.15.245.210 routes
Fri Feb 16 11:18:34.607 GMT
BGP router identifier 103.15.244.10, local AS number 58717
BGP generic scan interval 60 secs
Non-stop routing is enabled
BGP table state: Active
Table ID: 0xe0000000 RD version: 226519742
BGP main routing table version 226519742
BGP NSR Initial initsync version 2 (Reached)
BGP NSR/ISSU Sync-Group versions 226519742/0
BGP scan interval 60 secs
Status codes: s suppressed, d damped, h history, * valid, > best
i - internal, r RIB-failure, S stale, N Nexthop-discard
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 27.54.148.0/22 103.15.245.210 1000 0 133854 i
*> 27.54.148.0/23 103.15.245.210 1000 0 133854 i
*> 27.54.150.0/23 103.15.245.210 1000 0 133854 i
*> 43.224.108.0/23 103.15.245.210 1000 0 133854 i
*> 103.43.148.0/22 103.15.245.210 1000 0 133854 i
*> 103.43.148.0/23 103.15.245.210 1000 0 133854 i
*> 103.43.150.0/23 103.15.245.210 1000 0 133854 i
*> 103.100.233.0/24 103.15.245.210 1000 0 133854 i
*> 103.100.234.0/24 103.15.245.210 1000 0 133854 i
*> 103.100.235.0/24 103.15.245.210 1000 0 133854 i
*> 103.204.84.0/22 103.15.245.210 1000 0 133854 i

## Slide 11: Prefix adv.
RP/0/RSP0/CPU0:PALTAN-IIG-AGG#show bgp neighbor 103.15.245.34 advertised-routes
Fri Feb 16 11:24:23.886 GMT
Network Next Hop From AS Path
0.0.0.0/0 103.15.245.33 103.15.244.6 58717 9498i

## Slide 12: BW Policy
sh running-config policy-map 10023mb
% No such configuration item(s)
sh running-config policy-map 100mb
policy-map 100mb
class class-default
police rate 100 mbps burst 25 mbytes
conform-action transmit
exceed-action drop
!
!
end-policy-map

## Slide 13: MRTG
http://mrtg.summitiig.net

## Slide 14: Client end Nagois
others
file manager
etc
nagios3
objects
edit on customer.cfg
edit and save and close
others
customer commands
nagios service(restart)
http://103.15.246.18/nagios3
host
see the change
https://103.15.246.18:10000

## Slide 15: VC/CC Allow
Paltan Aggregation & DR Aggregation
sh ip access-lists VOIP-BLOCK
for cc:
Configuration
configure t
ipv4 access-list VOIP-BLOCK
461 permit ipv4 host 115.69.214.178 any
462 permit ipv4 any host 115.69.214.178
end
#SH RUN INT BE7
interface Bundle-Ether7
description @@ PALTAN-AGG-TO-PALTAN-CORE @@
ipv4 address 103.15.244.17 255.255.255.252
ipv6 address 2405:1500:0:2::41/126
ipv6 enable
bundle load-balancing hash dst-ip
load-interval 30
ipv4 access-group DROPBAND-WAN ingress
ipv4 access-group VOIP-BLOCK egress
!
#SH RUN INT BE4
interface Bundle-Ether4
description TO-DR-AGG
ipv4 address 103.15.246.210 255.255.255.252
ipv6 address 2405:1500:0:2::9/126
bundle load-balancing hash src-ip
load-interval 30
ipv4 access-group DROPBAND-WAN ingress
ipv4 access-group VOIP-BLOCK egress
!

## Slide 16: High latency/slow browsing
1.Check the geographical location of IP.
https://www.iplocation.net/
2. Ping status and trace report and problematic source IP block.
3.Check peering latency of upstream from smokeping
Smokeping: http://157.119.185.254/cgi-bin/smokeping.cgi?target=Destination
3. Check the routing
#sh bgp 203.117.155.202
BGP routing table entry for 203.117.0.0/16
Versions:
Process bRIB/RIB SendTblVer
Speaker 230612133 230612133
Path #2: Received by speaker 0
Advertised to update-groups (with more than one peer):
0.8
Advertised to peers (in unique update groups):
103.15.247.82
132602 2914 17645 4657, (received & used)
103.15.244.6 (metric 2) from 103.15.244.6 (103.15.244.6)
Origin IGP, metric 0, localpref 700, valid, internal, best, group-best
Received Path ID 0, Local Path ID 0, version 230612133
4. Change the routing
5. Forward trace and reverse trace
6. Check from client free lan block
7.Check the latency from looking glass:
https://www.ip-address.org/

## Slide 17: Packet loss,download/upload problem
1.Check Client BW utilization.
2.Check point to point packet loss.
3.Check peering packet loss of upstream from smokeping
Smokeping: http://157.119.185.254/cgi-bin/smokeping.cgi?target=Destination
4. Check packet drop from client source IP block.
6.Check the packet drop from looking glass:globally
https://www.ip-address.org/
7.Change upload/download path.
8.Communicate with upstream carrier.

## Slide 18: Youtube BW problem
1.Check Client BW utilization.
2.Check point to point packet loss.
3.Check with client BW wheather they are using SCL cache or not by browsing the below URL at client.
http://redirector.c.youtube.com/report_mapping

## Slide 19: Destination IP/Website unreachable
If we can access but client can’t:
Browse from SCL-IIG network
If we can browse ,take forward and reverse tracereport
take /30 IP block from client.
Check wheather the client source IP is blacklisted or not.
Client prefix advertisement change
Communicate with Upstream carrier with logs
If we both can’t access:
Check BTRC URL block
#sh route 185.38.150.8
Sun Feb 18 15:57:36.131 GMT
Routing entry for 185.38.150.8/32
Known via "bgp 58717", distance 200, metric 0, type internal
Installed Feb 14 10:39:08.872 for 4d05h
Routing Descriptor Blocks
103.15.244.14, from 103.15.244.14
Route metric is 0
No advertising protos
If not,then browse the website through other network
If the website is reachable through other network, then change the advertisement and route.

## Slide 20: BTRC URL Block
URL-SERVER:
IP: 103.15.245.106, SSH Port: 8022
Let's block "www.ipnewsbd.com"
vtysh (router mode)
advertise the destination network.
configure terminal
router bgp 58717
network 97.74.0.0/16
exit
exit
wr
exit
#check the advertisment to DC-AGG-RT
show ip bgp neighbors 103.15.244.10 advertised-routes
## For Domain:
iptables -A FORWARD -p tcp --dport 80 -m string --algo bm --string "ipnewsbd.com" -j DROP
iptables -A FORWARD -p tcp --dport 80 -m string --algo bm --string "www.ipnewsbd.com" -j DROP
FOR HTTPS:
iptables -A FORWARD -p tcp --dport 443 -m string --algo bm --string "ipnewsbd.com" -j DROP
iptables -A FORWARD -p tcp --dport 443 -m string --algo bm --string "www.ipnewsbd.com" -j DROP

## Slide 21: BTRC URL Block
## For URL: "www.india.com/bengali/world/omg-now-indians-can-join-bangladesh-army/"
iptables -A INPUT -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP
iptables -A OUTPUT -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP
iptables -A FORWARD -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP
#To see the URL at IP tables list
iptables -nvL
#To save the new URL at IP tables
iptables-save > /etc/sysconfig/iptables
#To delete:
iptables -D INPUT -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP
iptables -D OUTPUT -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP
iptables -D FORWARD -p tcp -m string --algo bm --string "/bengali/world/omg-now-indians-can-join-bangladesh-army/" -j DROP

## Slide 22: IP blacklisted
https://www.talosintelligence.com/
https://mxtoolbox.com/blacklists.aspx

## Slide 23: BGP shutdown/no shutdown
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config)#router bgp 58717
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config-bgp)#neighbor 103.15.245.210 shutdown
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config-bgp)#commit
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config)#router bgp 58717
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config-bgp)#no neighbor 103.15.245.210 shutdown
RP/0/RSP0/CPU0:PALTAN-IIG-AGG(config-bgp)#commit

## Slide 24: BW Fall
DHAKA CLIENT:
a)Case 1:BW FALL/Sudden DIP
1.Check MRTG graph for Client BW utilization and assigned BW
2.Check BGP status.
Command: sh ip bgp sum | I (client IP)
3.check received client prefix.
Command: sh ip bgp neighour (client IP) routes
4.If BGP is down then check with the client if they have done anything at client end and then check transmission path/physical link.
5.If BGP is up and don't receive any prefix then communicate with client to advertise the prefix.
6.If BGP is up and receive the prefix, then check if there is any upstream issue.
b)Case 2:Not getting proper BW or BW congestion or BW saturated
1.Check MRTG graph for Client BW utilization when the problem starts.
2.Check if there is any congestion in upstream.
3.Compare the MRTG graph utilization of previous 7days for the affected client.
Longhaul Client/Outside Dhaka Client except CTG:BW FALL/Not getting proper BW/BW fluctuation
1.Check MRTG graph for Client BW utilization.
2.Compare the MRTG graph utilization of previous 7days for the affected client.
3.Check point to point packet loss.if packet loss exists then communicate with NTTN.
4.Check if there is any upstream issue. If issue exists in upstream then please inform upstream responsible owner.

## Slide 25
Thank You